## Slide 1: Dynamic Charging Reaching goals in time

## Slide 2: Assessing technologies for climate friendly trucking involves several aspects
Criteria relevant for scaling up technologies and thus achieving the climate targets
  Operational range
  Time to market
  Scalability & resource efficiency
  Energy efficiency
  Total cost of ownership
  Flexibility
  CO2 abatement cost

## Slide 3: #operationalrange

## Slide 4: Range is especially important for long-haul operations
RF
FCEV
BEV
1,500
1,000
500
0
100%
0%
20%
40%
60%
80%
Mean motorway share
Daily mileage [km]
BEV: Battery electric vehicle | FCEV: Fuel cell electric vehicles | RF: Renewable fuel (for combustion engine)
Source: Fraunhofer feasibility study of catenary trucking, on behalf of the German Transport Ministry, page 131
  Journeys of 500 km or more are almost entirely on motorways (>80%)
Long range happens almost exclusively on highways

## Slide 5: #timetomarket

## Slide 6: Reaching political goals requires around 70% of truck sales in 2030 being zero emission
Chart: 
| 2016 | 2025 | 2030
Diesel | 100 | 93 | 30
Zero emission vehicles | 0 | 7 | 70
Share of new reg. semi-trucks [%]
Diesel
Zero emission vehicles
Analyses show that reaching key political goals (e.g., Paris Agreement, EU Fit-for-55, Germany’s national goal: 1/3 mileage using electricity) will require a 70% share of new semi-truck sales to be electrified zero emission trucks in 2030.
Those sales figures will only be met if sufficient infrastructure to power those trucks can be put in place by then.

## Slide 7: Overhead contact lines offers the most mature technical solution for long-haul heavy road freight
2021
FCEV
Fuel cell Electric Vehicle Announcement for start of serial production
Time to market for each technology in long-haul trucking
2022
2023
2024
2025
2026
2027
BEV
Battery Electric Vehicle Standardization of Megawatt charger planned to be completed
RF
Renewable Fuel Initial efuel production facility in operation
OCL
Overhead Contact Line Ready for roll-out

## Slide 8: #scalability

## Slide 9: Ramping up supply chains for catenary solution looks far less challenging than the alternatives
80
60
40
20
0
2020
2022
2024
2026
2028
2030
Mt
2020
2022
2024
2026
2028
2030
3,200
2,400
1,600
800
0
Kt of lithium carbonate equivalent
2020
2022
2024
2026
2028
2030
400
300
200
100
0
Kt
Copper
Lithium
Cobalt
Under construction
Operating
Production:
Sustainable Development Scenario (SDS)
Stated Policies Scenario (STEPS)
Primary demand:
Source: IEA The Role of Critical Minerals in Clean Energy Transitions (2021) page 119 | https://www.iea.org/reports/the-role-of-critical-minerals-in-clean-energy-transitions

## Slide 10: IEA: China dominates the entire downstream EV battery supply chain

## Slide 11: Role out of technology Based on cooperation across industries and development of open standards
https://www.continental.com/en/press/press-releases/20210729-ces-siemens-ehighway/
  EN50119 incl. informative annex C – OCL for electric trucks
  In the April 2020 update an Annex (informative) on infrastructure requirements for overhead contact lines for electric trucks on roads was already integrated.
  TC9x – Interaction between pantograph and OCL on electrified roads
  CENELEC working group (WG27) finalizing and reviewing a technical specification (TS) as initial step of a technical standard. TS expected in 6-9 months.

## Slide 12: International interest in dynamic charging is growing, e.g., in Europe Enabling zero emission trucking on core motorways, example countries
1. Nordics
  SE: National Transport Plan 2022 – 2034 includes planning for 2,400 km electrified motorways
  SE: Ca. 20 km pilot between national rail hub and nearby logistic centers being procured
  DK: Parliament approved €400 k study on overhead catenary (OCL) corridor to Germany
  NO: Public Road Administration study finds dynamic charging for trucks a cost-effective solution
2. UK
  Gvmt. funded £2 m feasibility study on ca. 20 km catenary pilot with 50 – 150 trucks
  Study finds catenary “most energy-efficient and cost-effective solution”, see also podcast
3. BeNeLux
  NL: Study finds most economical. Alignment with neighbors is very important
  BE: Study finds a very strong business case for overhead catenary
4. Central Europe
  AT: Study “Energy Roads” ongoing, with involvement of neighbors CZ and SK
  HU: Transport minster keen on implementing pilot project. Joint corridor study with AT & DE starting
  PL: Local government project proposal for catenary route in southern Poland
5. Mediterranean
  FR: Three Ministry-lead working groups on ERS: catenary is the cheapest solution for trucks
  IT: Ministry strategy for trucks focus on electrification, incl. use of catenary
  ES: Study by ECF finds TCO for overhead catenary already lower than ICE by 2025
Catenary solution: Demo/field trial realized or in preparation
Study with regard to catenary solution for HDV exists or under preparation
Interest in catenary solution exists
4
4
2
3
1
5
1
3
4
5
1
5

## Slide 13: #energyefficiency

## Slide 14: Direct electricity offers the most efficient way to use renewable energy
Large difference in energy efficiency impacts expected GHG-reductions and fuel cost savings
Adding losses in transport of fuel makes the difference even starker, especially for H2
Energy efficiency is key:
  Fuel cost large part of TCO
  Renewable energy still limited in availability

## Slide 15: #costofownership

## Slide 16: Cost of energy is by far the most important factor in the total cost picture
Source: https://www.plattform-zukunft-mobilitaet.de/wp-content/uploads/2020/12/NPM_AG1_Werkstattbericht_Nfz.pdf
Accumulated costs (2020 – 2050) in € bn (compared to fossil fuels)
Overall costs of carbon neutral road freight transport until 2050: energy costs of particular importance
Total cost
Vehicle
Energy infrastructure
Energy supply
0
25
50
75
100
125
150
175
200
Case study
Decarbonization of German long-haul freight transport
High cost scenario
Low cost scenario
RF
OCL
FCEV (PtG)

## Slide 17: NPM also sees electric solutions as near cost parity with diesel, far ahead of indirect alternatives in 2030
Source: https://www.plattform-zukunft-mobilitaet.de/wp-content/uploads/2020/12/NPM_AG1_Werkstattbericht_Nfz.pdf
Purchase price annuity
Insurance costs
Maintenance & repair costs
Energy costs
Costs of days lost
AdBlue costs
Infrastructure purchase
Total Cost of Ownership Semi Truck 40t (reference)
+94%
+23%
+5%
125,000
100,000
75,000
50,000
25,000
0
Diesel truck 2030
BEV truck 2030
OCL truck 2030
FCEV truck 2030
€ 2020/a
Where energy efficiency differs greatly the resulting energy costs also dominate the TCO calculation, e.g., almost half the TCO for FCEV is due to energy costs
Where energy efficiency is high, the cost of the vehicle dominate the TCO, e.g., almost half the TCO for a BEV is due to the purchase price
Truck for OCL with hybrid drive train slightly higher purchase price than diesel truck. However, a BEV truck for OCL would save on the combustion engine and not need as large a battery, and could be cheaper than a comparable diesel truck (see ECF report)

## Slide 18: #flexibility

## Slide 19: Decarbonization of heavy-duty trucks
    Technology options for trucks
    Key characteristics
    Preferred use case
Best for existing fleet decarbonization use case
Best for decarbonized urban distribution use case
Best for long range use case in which electrification is not economical
1 Assuming that a truck with hybrid-electric drive train is used | 2 Synthetic fuels require renewable energy for its production
Hydrogen fuel cell power
Battery electric power
Hybrid with synthetic/bio-fuel
High operational cost (e.g., due to fuel price, efficiency)
High range to mass ratio
Limited range
Technology eco-system proven with light duty vehicles
Limited availability of fuels
Available infrastructure, suitable to decarbonize existing fleet 1,2
H2

## Slide 20: Decarbonization of heavy-duty trucks will be possible with dynamic charging and an intelligent combination of drive train technologies
    Technology options for trucks
    Key characteristics
    Preferred use case
Best for existing fleet decarbonization use case
Best for decarbonized urban distribution use case
Best for long range use case in which electrification is not economical
1 Assuming that a truck with hybrid-electric drive train is used | 2 Synthetic fuels require renewable energy for its production
Hydrogen fuel cell power
Battery electric power
Hybrid with synthetic/bio-fuel
High operational cost (e.g., due to fuel price, efficiency)
High range to mass ratio
Limited range
Technology eco-system proven with light duty vehicles
Limited availability of fuels
Available infrastructure, suitable to decarbonize existing fleet 1,2
H2
All three drive train technologies and their business cases can be “boosted” by charging infrastructure such as “Overhead Contact Lines” (OCL) on major transit lines, similar to electric trains, reducing the cost per km.

## Slide 21: #CO2abatementcost

## Slide 22: NPM also sees electric solutions far ahead of indirect alternatives in 2030
Technologies where direct use of electricity is possible show an advantage of ca. 700 EUR per Tonne of CO2.
Policy measures can influence the relative TCO in the short term, but the global picture for most economical solutions is better shown by looking at the full abatement cost of each solution.
Chart: €2020/tCO2
| BEV-truck | FCEV-Fuel Cell truck | OCL
€2020/tco2 | 443 | 1164 | 441
Commercial vehicles >20t permissible total weight in 2030

## Slide 23: In summary: Dynamic charging is an essential solution for climate protection in heavy road freight transport It…
… is flexibly compatible with other technologies and fuels
… combines the benefits of electric railways with the flexibility of trucks
… changes the highway landscape
… is the most economical solution
… makes it possible to reach the climate protection goals
… can be realized in an international context
… can quickly be rolled out
eHighway
Notes: Image

## Slide 24
Hasso Grünjes Head of eHighway
Siemens Mobility GmbH
SMO RI EL COC EH
Erlangen, Germany
Mobil: +49 (173) 277 8387 E-mail: hasso.gruenjes@siemens.com
www.siemens.com/ehighway
#eHighway

## Slide 25: Proven in daily trucking operations on German motorways
Motorway owner’s experience of field trial
Experiences of an eHighway-truck driver
https://www.youtube.com/watch?v=NHSofIc31rw
https://www.youtube.com/watch?v=gAUff-fz_MM&t=0s

## Slide 26
Available online
Factsheet for climate-friendly road freight